## Slide 1: IOT Smart Drone
Peidong Chen, Yitian Hu, Yang Yang, Jiayu Guo
Advisor: Prof. William Kaiser
EE202C Networked Embedded Systems Design Midterm
Notes: introduce group members

## Slide 2: Mid-term Progress Presentation
Background and Mission
Design Overview
Technical Details:
a. Drone system
b. IOT functionality
Test & Verification
Future Plan
Team Responsibility & Reference Resource
Notes: today's presentation would include these following things->
why iot drone?
issues to solve and difficulties
focus on technical details
test reliability and performance /show demo

## Slide 3: Product Development Mission Background: Flying nodes
Flying hotspot (agriculture)
Logistics ( Amazon delivery)
Real-time Traffic& security monitoring
"Dr. Parimal Kopardekar, the manager of NASA's NexGen concepts and technology development project"
Notes: This network system is also likely to be cloud-based,
meaning that drones will need an internet link to download information
about weather, logistics, traffic((flow speed) and restricted zones.​

## Slide 4: Flying hotspot
http://hplusmagazine.com/2015/03/19/future-farming/
Product Development Mission Background: Flying nodes
Notes: For farms, we always do not have wifi access to outdoor sensors and gateways.

## Slide 5: Logistics
Amazon drone
Product Development Mission Background: Flying nodes

## Slide 6
Traffic monitoring
A police officer stands next to a fake "Speed Enforced By Drones" sign found on a California highway.
Product Development Mission Background: Flying nodes
UAV Monitoring Traffic

## Slide 7: Design Overview: Technical Challenges
Detailed Problem Statement
  Battery life time & Power consumption
  Alleviated by charge station information on the Internet
  Data transmission online
  Whether real-time and high-speed
  Drone reliability and safety with multi-functionality
  Test by building a drone by ourselves

## Slide 8: System Architecture
Drone system
PWM generation
Gyroscope detection
IOT functionality
Cloud server data analyzing
Evasion avoidance
Ultrasonic sensor
PID controller
Image Processing
Auto navigation

## Slide 9: Drone system
I2C issues in Yocto >= 2.1
GPIO
GPS ultimate adafruit
uart
Notes: PWM signal in Edison cannot provide a resolution higher than 8bits, which is only equal to 12 levels for motors.

## Slide 10: Design Overview: Technical Approach
Detailed Approach: hardware
Installment
9dof sensor
PMW generation
Ultrasonic sensor
Madgwick AHRS

## Slide 11: Design Overview: Technical Approach
Detailed Approach: hardware
  PID controller
  3D printing protector and connector
PID controller
3Dprinting
Notes: In this model, P accounts for present values of the error (e.g. if the error is large and positive, the control output will also be large and positive), I accounts for past values of the error (e.g. if the output is not sufficient to reduce the size of the error, error will accumulate over time, causing the controller to apply stronger output), and D accounts for predicted future values of the error, based on its current rate of change

## Slide 12: Design Overview
Full-size linux server
  MySQL for database
  HTTP Restful api
  Sockets for video transmitting
Mobile Device
  Sending commands
  Monitor sensors' status
Notes: For the software part, we use full-size linux server to

## Slide 13: Design Overview
  The code is written in C and has more than 4 threads.
  The robotic will send/receive commands/data from the server in one thread.
  We have separate threads for reading each sensor's data maintain the flying state.
Notes: For the software part, we use full-size linux server to

## Slide 14: Design Overview: Technical Approach
Detailed Approach: software
  Main functionality
information transfer diagram

## Slide 15: Design Overview: Technical Approach
Detailed Approach: software
  GPS navigation
    Get Destination GPS from server
    From Adafruit ultimate GPS and gyro get GPS and direction of drone
    Compute latitude and longitude distance separately
Notes: we compute the two distance coninuously, and then find the destination direction.
Our can we firstly turn to the right direction and then start to move forward

## Slide 16: Design Overview: Technical Approach
Detailed Approach: software
  Surf algorithm
    Using Hessian Matrix to find points of interests
Notes: The determinant of the Hessian matrix is used as a measure of local change around the point and points are chosen where this determinant is maximal
SURF also uses the determinant of the Hessian for selecting the scale, as it is done by Lindeberg. Given a point p=(x, y) in an image I, the Hessian matrix H(p, σ) at point and scale σ, is defined as follows:

## Slide 17: Design Overview: Technical Approach
Detailed Approach: software
  Surf algorithm
    Using Hessian Matrix to find points of interests
    To speed up, using box filter to do approximates
    From Haar wavelet responses in both x- and y-directions get the orientation
    Compute vector inner product
    to find the match point
Notes: The determinant of the Hessian matrix is used as a measure of local change around the point and points are chosen where this determinant is maximal
SURF also uses the determinant of the Hessian for selecting the scale, as it is done by Lindeberg. Given a point p=(x, y) in an image I, the Hessian matrix H(p, σ) at point and scale σ, is defined as follows:
The Haar wavelet responses in both x- and y-directions within a circular neighbourhood are computed. The obtained responses are weighed by a Gaussian function centered at the point of interest,he dominant orientation is estimated by calculating the sum of all responses within a sliding orientation window of size π/3
This orientation feature can help find the rotated object

## Slide 18: Testing and Verification
Test and Verification Plan
  App test bench
  Drone stability test
  IOT algorithm test

## Slide 19: Future Plan
Solve the i2c bus freeze problem and fly the drone stably;
Improve our algorithm and attach GPS navigation to the drone;
Fulfill and implement the object detection section to the drone.

## Slide 20: Future Plan
Detailed Approach:
Notes: This is our plan for doing the car tracking function.
The car is moving and sending its location to the server. When we use iPhone to send commands to begin the tracking program. The drone contacts the server to get the car's location within 10 meters.
When the drone goes to the location, it will use the camera to send images to the server. And using the cloud computing, the server can find out the specific location of the car. And guide the drone to follow the car.

## Slide 21
Thank you!
Notes: especially thank for Professor Kaiser and Chris's help! thx for all your listening.

## Slide 22: Team and Responsibilities
  Peidong Chen: Server side API design, Edison side function programming with multi-threads, camera images uploading and server side detection.
  Yang Yang: IOS app, GPS navigation, figure object detection, Edison side function programming
  Jiayu Guo: 3D printing; build the drone; GPS/ultrasonic setup; test the drone
  Yitian Hu: 3D printing; build the drone and set up sensors and processor boards; read 9-dof MPU9250 sensor and get sensor fusion data

## Slide 23: Resources and References
https://github.com/peidong/drone
An efficient orientation filter for inertial and inertial/magnetic sensor arrays
Sebastian O.H. Madgwick April 30, 2010