## Slide 1
EE202C IoT Smart Drone
UCLA
Peidong Chen, Yitian Hu, Yang Yang, Jiayu Guo
Advisor: Prof. William Kaiser

## Slide 2
The IOT functions:
GPS navigation and object tracking by image processing
  Amazon delivery
  Fugitive detecting and tracking

## Slide 3
System Architecture (Before)

## Slide 4
System Architecture (Before)

## Slide 5
System Architecture (Before)

## Slide 6
System Architecture (Now)

## Slide 7
Edison Software Flowchart
Start
Thread 1:
Http get commands, send to BBB
Thread 2:
Http get pid parameters
Thread 3:
Receive messages from beaglebone
Thread 4:
Http post data to server
Thread 5:
GPS Navigation
Process 1
(C code)

## Slide 8
Edison Software Flowchart
Start
Thread 1:
Http get image detection and GPS info
Thread 2:
Http post images to server
Thread 3:
Send commands to beaglebone
Process 2
(Python)

## Slide 9
Beaglebone Black ( Flight controller )
Start
Thread 1:
Generate 16-bit PWM
Thread 2:
Read gyro
Thread 3:
Receive messages from Edison
Thread 4:
PID feedback
Thread 5:
Read GPS and send it to Edison

## Slide 10
Beaglebone Black
Since there is no Internet access for Beaglebone,it should start the flight controller functions when it boots.

## Slide 11
Server REST API
Commands
GET api/control
POST api/control
PID tuning
GET api/pid_tuning
POST api/pid_tuning
GPS
GET api/gps
POST api/gps
Camera
GET api/camera
POST api/camera
Written in PHP

## Slide 12
GPS Location Tracker
GPS
Send info to GPS tracking server
Server
HTTP
UART
UART
Server
"GPRMC"format
Ubidots:

## Slide 13
GPS Tracker Demo
https://www.youtube.com/watch?v=biHrlLmg0Tg

## Slide 14
Flight Position Control
Flight Mode Control
Auto_flight()
Manual_flight()
Stop_flight()
Set yaw,pitch, raw value
Motor Output

## Slide 15
Series PID Design&Tuning
One Loop Angle PID controller
{Imperfection:
integral wind-up
Real world derivative noise
Code generated decay&spike}
Yaw Pitch Roll PID controller
Angular velocity PID controller
ESC propeller module
9 Dof sensor
filter
MARG
filter
Gyro:Ω​​​
1/s
Θ
Angular input reference
Outer Loop Angle PID & Inner Loop Angular velocity PID controller
Non-symmetric/large signal
Higher sampling rate

## Slide 16
Series PID
PIDsetsetpoint();
PIDsettunings();
PIDRun();
pidData->output= pidData->prevOutput+
pidData->zKp*pidData->error+ pidData->iTerm+pidData- >dTerm;
Noise Filter&Calibration
1.Kalman filter
2.MARG (mag/gyro)
3.Simple round process
< 0.6 ◦ RMS error;

## Slide 17
PID tuning Demo
https://www.youtube.com/watch?v=M6bZd2e6u7M

## Slide 18
Detection and Follow
Detector
Follower
Get reference image
Send GPS information
Reference image
Object location
Lost object
Movement Command

## Slide 19
Detector
Surf Algorithm:
Receive reference image from server
Find object according specific features
Send location information to tracker

## Slide 20
Tracker
Camshift Algorithm:
From initial location get the target distribution
Do histogram backproject to generate the probability image
Weight and ratio the histogram
Iterate Mean shift to find the centroid location and reccord 0th moment
Update location
Update the window size using 0th moment

## Slide 21
Detection Demo
https://www.youtube.com/watch?v=s-hM2iVRJzo

## Slide 22
Accuracy detection algorithm
Deep learning algorithm: fast rcnn
HOG + SVM for human detection

## Slide 23
Searching
Detection and following model
Keep sending pictures and GPS
Accuracy detection algorithm
Images
Save reference image
Send command to all near by drone
Send reference image
Detection nearby using GPS

## Slide 24
Problems and Future Work
Integrate GPS navigation, detection and tracking functions to drone when it can fly
Finish the fly video in around one week
Reading GPS data and sending commands via the only one UART can randomly cause Edison to reboot.
Problems
Future work

## Slide 25
Thank you